5.1 Link Layer: Introduction and services
Nodes = computers or routers
links = the links between all these nodes

The services provided by the link layer
frames = units of data exchanged by link layer protocol
Examples of link layer protocols: Ethernet, WiFi, token ring and PPP

Link layer protocol encapsulates network layer
On the link layer only direct links are used for sending fro source to destination and every time different services are used:

1. Framing: Placing a header (and trail) to the network datagram
2. Link Access. In case of multiple active nodes the MAC protocol is used to give the right link access ( Medium Access Control)
3. Reliable delivery. Works the same way as TCP in case of reliable delivery. Is important in cases like wireless, but has too much overhead in case of wired transmission. Is used so that not at the TCP level alone the errors can be detected
4. Flow control. Not overwhelming the receiver with too much data, just like in the transport layer
5. Error detection. Bit checking to be certain no errors occurred. In case of transport layer en network layer this is done by checksum, but in case of link layer this is more sophisticated
6. Error correction.
7. Half duplex and full duplex. Full duplex = both sides can transmit at the same time. Half duplex: A node cannot both transmit and receive at the same time

Most services are the same as on the transport layer . Differences:
-Reliable data is now not tested between end to end hosts but on a single link
-Same for flow control; only between links in case of the link layer

    1. Where is the link layer implemented?
Link layer is implemented on the NIC ( Network Interface Card). So functionality is mostly in hardware. Software side = receiving the datagram from the network layer, assembling addressing information for the link layer, activating the controller hardware. On the receiving software side= responds to interrupts from the controller(reception from frames)m handling errors and sending to the network layer

  1. Multiple Access Protocols
Multiple access problem = How to send a packet to multiple nodes (by broadcast)
Multiple Access Protocol = Rules with which nodes regulate their transmission into the shared broadcast channel.
In case of a collission all messages are lost ( cause they got entangled)

For Multiple accress protocols . If a broadcast channel has a rate of R bps than:
1. When only one node is sending, than that node has a throughput of R bps
2. When M nodes have data to send the throughput for each node is R/M
3. There is no master node that represents a single point of failure for the network
4. it should be simple

Three categories: Channel partitioning protocols, Random Access Protocols, Taking turns protocols

    1. Channeling partitioning protocols
WDM and TDM (You already know about these!

    1. Random Access Protocols
A transmitting node always transmits on full rate. If threre is a collision, each node waits for a random amount of time after which they start rapidly retransmitting the collisioned packets. Because of the random delays one of the colliders will now be able to sneak in its packets before the other

Slotted ALOHA
Simple random access protocol
- All frames L bits
- Time is divided in slots of L/R seconds(slot equals time to transmit one frame)
- Nodes transmit only at beginning of slot
- In case of collision all sending nodes use a independent probability if they will send again in the next slot.
- Only succees if one node sends in one timeslot.
The chance a given node does transmit and the rest does not = p(1-p)^N-1
And this in case of all nodes Np(1-p)^N-1
Succesful tranmission in only 0.37 R

Carrier Senses Multiple Access
Listen before speaks = Carrier Sensing
If someone else starts talking at the same time stop talking = Collision Detection

because of propagation delay it can be so that two hosts start sending.