1.3

Two approaches to moving data through a network

circuit swithching
- reserves a connection for a given duration
- reserves bandwidth for communication between hosts, has a guaranteed rate

packet switching
- no reservation needed
- Is todays internet
- Best effort. Delays can happen cause nothing is reserved or guaranteed

Circuit Switchint
In case of circuit switching, if there are possible n simultaneous connections, one link ca have a fraction 1/n of the total available bandwidth for its reservation

Multiplexing in circuit-switched networks
Two ways:
-Frequency Division Multiplexing
A frequency is devided in multiple ranges to broadcast over
-Time Division Multiplexing
time is devided in slots in which every slot consists of a sender receiver pair that is reserved for. A frame in these slots is one timestep.

Arguments against circuit-switching: It is wasteful in case a sender-receiver pair had reserved space but is not using any space = Silent period

packet switching
mostly store and forward=switch must first receive entire packet before starting to send data forward

How long does it take to send a packet over the network?
L = bits to send
Q = links between two hosts
R = rate of network in bps

total delay is QL/ R

Packet switching versus circuit switching:statistical multiplexing
Packet switching does not seem suitable for real time servers and circuit switching is wasteful in resources

Why is packet switching more efficient?
Example :
1 mbps link
users 10 procent of the time 100 kpbs
90 procent of the time 0
in case of TDM, 1 frame can be 10 slots of 100 kpbs. Now only 10 people can make use of the internet at a time, while a lot is wasted
statistical multiplexing =allocating data on the go (on-demand sharing of resources)

ISPs and internet backbones
Internet is a network of networks. The edge Internet Service Providers(like universities and companies etc.) are situated in a tiered structure of ISPs
Access ISPs are at the bottom of the hierarchy (tier 3)

Tier 1 ISPs:
-Tier 1 ISP is the same as any other network but with very fast connection
- Are connected to all other tier 1 ISPs
- connected to large amound of tier 2 ISPs and other customer networks
- international in coverage
- Also called as internet backbone networks
Tier 2:
- National coverage
- connects only to a few tier 1 ISPs
- Tier 2 is customer of Tier 1 to which it is connected, tier 1 is the provider of tier 2
- Can also connect to other tier 2(peering)
But : some tier 1 providers are also tier 2 providers and sell internet access directly to end users

points of presence= point of connections between ISPs

Types of delay
Processing delay
The delay that occurs when checking header and errors in the packet(very small

Queueing delay
Waiting for other packets to be transmit that arrived earlier at the router. Varies immensely

Transmission Delay
delay of putting a packet onto the link (store and forward)
S = size packet
R = transmission rate
transmission delay = S/R

Propagation delay
The delay
if l = propagation speed of medium
k = length of cable
propagatuin delay = k/l

Queueing:
Traffic intensity = La/R
where R = transmission rate
L = bits per packet
a = packets/sec
if La/R < 1 = :)
else bad!

Instanteneous througput= the rate at which host B is receiving a file from host A if file consists of F bits and sending takes T seconds the average throughput is F/T
The throughput depends on the slowest link when transmitting data
transmission rate is the rate of the bottleneck link

The bottleneck can also become the internet link because it is heavily used by other computers as well

Why layering?
Easier to change little things

why not layering?
Duplicate functionallity among layers

layers: (protocol stack)
application
transport
network
link
physical